## Slide 1
RECYCLING OF WASTE PAPER
In the Paper Industry
From Recovered Paper to Recycled Pulp — Process, Equipment & Key Parameters
Collect
Sort
Pulp
Screen
Clean
Deink
Refine
Paper

## Slide 2
WHY IT MATTERS
Why Recycle Waste Paper?
Saves Trees
Reduces virgin
fibre demand
Saves Water
Lower fresh-water
intake vs virgin pulp
Saves Energy
Less energy than
pulping virgin wood
Cuts Landfill
Diverts waste paper
from disposal
Recycled fibre can typically be reused several times before fibre strength limits further recycling.
Waste-Paper Recycling | Paper Mill Process
2

## Slide 3
PROCESS FLOW
Main Process Flow
Collection
Sorting
Bale
Opening
Pulping
Screening
Blending
Refining
Thickening /
Washing
Deinking
Cleaning
PAPER MACHINE — Form, Press & Dry
Waste-Paper Recycling | Paper Mill Process
3

## Slide 4
STAGE 01
Collection & Sorting
Separate recovered paper by grade before it enters the mill
OCC
Old Corrugated
Containers
ONP
Old
Newspapers
Office Paper
Sorted white /
ledger grades
Mixed Paper
Assorted low-grade
recovered paper
Waste-Paper Recycling | Paper Mill Process
4

## Slide 5
STAGE 02
Bale Opening & Pulping
Bale Opening
Bales opened & fed to stock prep
Feeds waste paper into system
Pulping (Hydrapulper)
Paper mixed with water
Broken down into individual fibres
Junk trap removes large debris
Waste-Paper Recycling | Paper Mill Process
5

## Slide 6
STAGE 03
Screening & Cleaning
Progressive contaminant removal — coarse to fine
Coarse Screening
REMOVES
Plastics · Strings · Tapes · Large debris
Cleaning
REMOVES
Sand · Glass · Metals (centrifugal cleaners)
Fine Screening
REMOVES
Small contaminants · Stickies
Waste-Paper Recycling | Paper Mill Process
6

## Slide 7
STAGE 04
Deinking & Flotation / Washing
Removing printing ink to restore brightness and cleanliness
1
Deinking
Printing ink is dislodged from fibre surfaces where required
2
Flotation
Air bubbles carry ink particles to a froth layer for removal
3
Washing
Separates ink particles and dissolved contaminants from pulp
Waste-Paper Recycling | Paper Mill Process
7

## Slide 8
STAGE 05
Thickening, Refining & Blending
Preparing recycled pulp for the paper machine
Thickening
Increases pulp
consistency
Refining
Develops fibre strength
& bonding properties
Blending
Mixed with virgin pulp
& additives as required
Waste-Paper Recycling | Paper Mill Process
8

## Slide 9
FINAL STAGE
Paper Machine
Recycled pulp becomes new paper or board
Form
Fibres deposited into a wet sheet
Press
Water mechanically removed
Dry
Heated cylinders dry the sheet
Finished Paper
New paper / board product
Waste-Paper Recycling | Paper Mill Process
9

## Slide 10
EQUIPMENT
Major Equipment
Bale Handling System
Hydrapulper
Junk Trap
Coarse & Fine Screens
Centrifugal Cleaners
Deflakers
Deinking Flotation Cell
Disc Filter / Thickener
Disperser
Refiner
Reject Handling System
Sludge Dewatering System
Waste-Paper Recycling | Paper Mill Process
10

## Slide 11
CHALLENGES
Main Problems in Waste-Paper Recycling
Contaminants
Plastic, staples, tape, glass, sand, metals
Stickies
Adhesives from labels & packaging
Ink
Affects brightness & cleanliness
Fibre Deterioration
Repeated recycling weakens fibres
High COD / BOD
Dissolved organics in wastewater
Rejects & Sludge
Require disposal or recovery
Energy & Water Use
Pulping, screening, deinking are utility-intensive
Waste-Paper Recycling | Paper Mill Process
11

## Slide 12
QUALITY CONTROL
Key Parameters to Monitor
Pulp Consistency
Freeness (CSF)
Brightness
Dirt Count
Ash
Moisture
Reject %
Fibre Yield
Stickies
COD / BOD
pH
Chemical Use
Fresh-Water Use
kWh / ton Pulp
Waste-Paper Recycling | Paper Mill Process
12

## Slide 13
MATERIAL BALANCE
Typical Material Balance
Illustrative split for 1,000 kg of waste paper processed — actual yield depends on grade & process
1,000 kg
Waste Paper
Chart: kg (per 1,000 kg input)
| Usable Recycled Fibre | Rejects | Sludge | Process Losses (water/steam)
Material Balance | 750 | 130 | 70 | 50
Waste-Paper Recycling | Paper Mill Process
13

## Slide 14
Sustainability & Compliance
ISO 14001 — Environmental management of effluent, sludge & emissions
ISO 50001 — Structured energy monitoring across pulping, screening & deinking
Continuous tracking of water, energy & reject % supports both standards
Next Step
A dedicated 10–15 slide deck can expand each section with your mill's own energy, water, ETP and material-balance data.
Thank You
Waste-Paper Recycling | Paper Mill Process
14